## Slide 1: CSS 422 Hardware and Computer Organization
Combinational Circuit
CPU Components and ALU Design
Professor: Munehiro Fukuda
Ver. 2

## Slide 2: Topics
Karnaugh Map: more simplification techniques
Digital Components
  Multiplexer
  Decoder
  Comparator
ALU Design
  Half/Full Adders and Subtraction
  Multiplier
  ALU
Berger: Ch 1, 2, and 3
Null: Ch3

## Slide 3: More Karnaugh Map Technique Use of Negation
If you find many 1s, group 0s.
Add a negation of the sum (= OR)

## Slide 4: More Karnaugh Map Technique Exclusive OR
If a Kmap shows a latice with 0 at the upper left cell, use an exclusive OR.
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 1
1 | 0
B 0 1
A
0
1
Kmap
1 | 0
0 | 1
B 0 1
A
0
1
Kmap
0 | 1 | 0 | 1
1 | 0 | 1 | 0
BC 00 01 11 10
A
0
1
Kmap
0 | 1 | 0 | 1
1 | 0 | 1 | 0
0 | 1 | 0 | 1
1 | 0 | 1 | 0
CD 00 01 11 10
AB
00
01
11
10
Kmap
truth table
F1 = A~B + ~A B
= A B
F2 = ~F
= ~(A B)
F3 = A B C
F4 = A B C D

## Slide 5: More Karnaugh Map Technique Don’t Care Terms
If some products can be either 0 or 1, you can choose 0 or 1 as you create larger groups.
0 | 0 | 0 | X
0 | 1 | X | 0
X | X | 1 | 1
0 | 0 | 0 | 0
CD 00 01 11 10
AB
00
01
11
10
Kmap
A | B | C | D | P
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | X
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | X
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | X
1 | 1 | 0 | 1 | X
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 1
0 | 0 | 0 | 0
CD 00 01 11 10
AB
00
01
11
10
Kmap
F = AB + BD

## Slide 6: Product of Sums
Simplification Steps
  Negate a given product-of-sums form.
  Apply De Morgan’s law to the negation.
  Draw the corresponding truth table and Kmap.
  Get a simplified logic.
  Re-negate it back.
Example
  F = (A + B + C)(B + ~C)
  ~F = ~{(A + B + C)(B + ~C)}
  = ~(A + B + C) +~(B + ~C)
  = ~A~B~C + ~BC
  Truth table and Kmap
  ~ F = ~A~B +~BC
  F = ~(~A~B + ~BC)
  = ~(~A~B)~(~BC)
  = (A + B)(B + ~C)
1 | 1 | 0 | 0
0 | 1 | 0 | 0
BC 00 01 11 10
A
0
1
A | B | C | P
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0

## Slide 7: Simple Multiplexer (MUX)
The MUX circuit allows one of two ( or more ) logical signals to be selected
Bus Selection
ALU Design

## Slide 8: Multiplexers
A, B, C is control lines so that which of the eight input lines to be gated.
(a) An eight-input multiplexer. (b) The same multiplexer wired to compute the majority function.
Bus Selection
ALU Design

## Slide 9: Decoder
A 3-to-8 decoder circuit: Depending on the inputs, only one of eight outputs is 1.
Interrupt Control Hardware

## Slide 10: Comparator
A simple 4-bit comparator.
ALU Design

## Slide 11: 1-Bit Left/Right Shift Register
ALU Design

## Slide 12: Half Adder
A | B | Carry | Sum
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
1-bit addition
A + B = Sum
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 1 0
Truth Table
~AB
A~B
S = ~AB + A~B = A + B
C = AB
ALU Design

## Slide 13: Full Adder (1)
A | B | Cin | Cout | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Truth Table
0 | 1 | 0 | 1
1 | 0 | 1 | 0
AB 00 01 11 10
Cin
0
1
Kmap for S
0 | 0 | 1 | 0
0 | 1 | 1 | 1
AB 00 01 11 10
Cin
0
1
Kmap for Cout
Can’t simplify the logic at all:
S = ~A~BCin + ~AB~Cin + A~B~Cin + ABCin
Use the algebrical laws:
S = (~AB + A~B) ~Cin + (~A~B + AB) Cin
= (A B)~Cin + (~(A+B) + ~(~A + ~B))Cin
= (A B)~Cin + ~((A+B)(~A + ~B))Cin
= (A B)~Cin + ~(A~A +A~B+~AB +B~B)Cin
= (A B)~Cin + ~(A~B+~AB)Cin
= (A B)~Cin + ~(A B)Cin
= A B Cin
If a Kmap became a lattice,
It means exclusiv ORs
Cout = AB + BCcin + CinA
Use the algebrical laws:
Cout = AB(Cin + ~Cin) + (A +~A)BCin + A(B + ~B)Cin
= ABCin +AB~Cin + ABCin +~ABCin + ABCin + A~BCin
= ABCin + AB~Cin + (~AB + A~B)Cin
= AB(Cin + ~Cin) + (A B)Cin
= AB + (A B)Cin
ALU Design

## Slide 14: Full Adder (2)
1-bit full addr
A
B
Cout
Sum
Cin
A
B
Cout
Sum
Cin
A
B
Cout
Sum
Cin
A
B
Cout
Sum
Cin
GND
A0
B0
A1
B1
A2
B2
A3
B3
4-bit full addr
Propagation Delay (with ripple carry)
7483 4-bit full addr
Carry look ahead
ALU Design

## Slide 15: Subtraction
A – B = A + (–B) = A + (~B + 1)
2’s complement
ALU Design

## Slide 16: Multiplier
A1 A0
x) B1 B0
C1 A1B0 A0B0
+ +
+) A1B1 A0B1
P2 P1 P0
Full Addr
Half Addr
ALU Design

## Slide 17: ALU
F0 | F1 | Operations
0 | 0 | AB
0 | 1 | A + B
1 | 0 | ~B
1 | 1 | A plus B
ALU Design

## Slide 18: 4-bit ALU
F0
F1
Cout
Cin
Ripple Carry
74181: Carry Look Ahead
ALU Design

## Slide 19: Summary
More Kmap Techniques
  Use the negation, XORs and “don’t care” terms
Digital Components
  Multiplexer: choosing a data line from memory chips
  Decoder: choosing a memory chip
Design of ALU
  Comparator and shift register
  Half/Full adder
  Subtraction using a full adder (with ~B + Cin)
  Multiplication with two half adders
  Ripple carry versus carry look ahead Adder/ALU