## Slide 1: CSS 422 Hardware and Computer Organization
Combinational Circuit
Logical Gates and Karnaugh Map
Professor: Munehiro Fukuda
Ver. 2

## Slide 2: Topics
Logic and Gates
  From circuit to logic
  From logic to circuit
Canonical Forms
  Sum of products
  Product of sums
Karnaugh Maps and Boolean Equation
Berger: Ch 1, 2, and 3
Null: Ch 3

## Slide 3: Analog vs Digital Circuits
Analog
Values: Any level probably between 0 and 5 volts
Signal Transmission
Example
Digital
Values: Two states
  5V = H = 1 = On, 0V = L = Off
Signal Transmission
Example
circuit
circuit
1 1 0 1
Vcc (5V)
Input
High = 2.0 ~ 5V
Low = 0 ~ 0.7V
Output
GND
Collector
Base
Emitter

## Slide 4: Logical Gates
AND | OR | NOT

## Slide 5: More Logical Gates
74 series
7408
7432
7402
7400
7402
7486
In general, integrated circuits consist of these basic logical gates.

## Slide 6: Boolean Algebra and Logical Gates
Axiom
Theorem

## Slide 7: De Morgan’s Law

## Slide 8: From circuit to Boolean Logic
We can easily interpret the function of a given circuit.
Ex)
A
B
A
B
A
B
A*
B
A *
B
C
A *
B
+
A *
B
C = A + B

## Slide 9: From Boolean to Circuit

## Slide 10: 3 x 8 Line Decoder (2)
a | b | c | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
    abc = 100 --- D4 =1
    abc = 101 --- D5 =1
    abc = 110 --- D6= 1
    abc = 111 --- D7= 1
    abc = 000 --- D0 =1
    abc = 001 --- D1 =1
    abc = 010 --- D2= 1
    abc = 011 --- D3= 1

## Slide 11: 3 x 8 Line Decoder (3)
    D0 = ~a ~b ~c
    D1 = ~a ~b c
    D2 = ~a b ~c
    D3 = ~a b c
    D4 = a ~b ~c
    D5 = a ~b c
    D6 = a b ~c
    D7 = a b c

## Slide 12: Canonical Form: Sum of Products
F = AB~C + A~BC + ~ABC
(where ~ = NOT)
Through De Morgan’s Law, the circuit can consist
of ony NANDs (with Nots)
product
sum

## Slide 13: Canonical Form: Product of Sums
F = (~A+~B+~C)(A+B+~C)(A+~B+C)
(where ~ = NOT)
Through De Morgan’s Law, the circuit can consist
of ony NORs (with Nots)
sum
product

## Slide 14: Circuit Design: Sum of Products
Circuit Design Steps
  Create a truth table.
  Identify all products that output “H” or 1.
  Create a sum-of-products form.
  Design the corresponding logical circuit with ANDs and ORs.
Disadvantages
  Many ANDs
  Many inputs to the OR
Logic Simplification
  Convert a truth table into a Karnough map.
  Group neighboring products.
C | B | A | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Design a 3-input majority circuit.
F = AB~C + A~BC + ~ABC + ABC
AB~C
A~BC
~ABC
ABC

## Slide 15: Karnaugh Map - Creation
How to convert a truth table (w/ 2-4 inputs) into a Karnaugh map
A | B | C | D | P
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 0
0 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 0 | 1 | 0
CD 00 01 11 10
AB
00
01
11
10
A | B | P
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
1 | 0
1 | 0
B 0 1
A
0
1
A | B | C | P
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
0 | 1 | 0 | 0
1 | 1 | 1 | 1
BC 00 01 11 10
A
0
1
4 inputs
truth table
Kmap
2 inputs
3 inputs
truth table
truth table
Examples
Kmap
Kmap

## Slide 16: Karnaugh Map - Simplification
Simplification Steps
  Group neighboring products.
  Assign AND to each group.
  Create a sum-of-products form.
  Design the corresponding logical circuit.
1 x 2 or 2 x 1 rectangular group | 1 x 4 or 4 x 1 rectangular group
2 x 4 or 4 x 2 rectangular group | 2 x 2 square group
Key 1: Get a larger group – reducing #inputs of the AND gate
Key 2: Reduce # groups – reduing # AND gates
1 |  |  | 1
 |  | 1 | 
 |  | 1 | 
CD 00 01 11 10
AB
00
01
11
10
1 |  |  | 1
1 |  |  | 1
1 | 1 | 1 | 1
1 | 1 | 1 | 1
CD 00 01 11 10
AB
00
01
11
10
1 | 1 | 1 | 1
1 |  |  | 
1 |  |  | 
1 |  |  | 
CD 00 01 11 10
AB
00
01
11
10
1 |  |  | 1
 | 1 | 1 | 
 | 1 | 1 | 
1 |  |  | 1
CD 00 01 11 10
AB
00
01
11
10
~AB~D(C+~C)=~AB~D
A(B+~B)CD=ACD
~A~B(~C~D+~CD+CD+C~D)
=~A~B{~C(~D+D)+C(D+~D)}
=~A~B(~C+C)
=~A~B
~C~D
~D
~A
~B~D
BD

## Slide 17: Eg 1: 3-Input Majority Circuit
C | B | A | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
F = AB~C + A~BC + ~ABC + ABC
AB~C
A~BC
~ABC
ABC
 |  | 1 | 
 | 1 | 1 | 1
BA 00 01 11 10
C
0
1
Kmap
truth table
AC
BC
AB
F = AB + BC + CA

## Slide 18: Eg 2: Boolean Simplification with K-Map versus Algebraic Laws
A B C x
x = B*C + A*B + A*C
Simplified equation
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
1 |  |  | 
1 | 1 | 0 | 1
BC 00 01 11 10
A
0
1
Kmap
A~B
A~C
~B~C

## Slide 19: Eg 3: 4-Input Circuit Simplification with K-Map versus Algebrical Laws
A B C D X
0 0 0 0 0
1 0 0 0 0
0 1 0 0 0
1 1 0 0 1
1 1 1 0 1
0 0 1 0 0
1 0 1 0 1
0 1 1 0 0
0 0 0 1 1
1 0 0 1 0
0 1 0 1 1
1 1 0 1 0
0 0 1 1 1
1 0 1 1 0
0 1 1 1 1
1 1 1 1 0
X = ~A*D + A*B*~D +A*C*~D
1. X = A*B*~C*~D + A*~B*C*~D + A*B*C*~D + ~A*~B*~C*D + ~A*B*~C*D + ~A*~B*C*D + ~A*B*C*D
2. X = A*B*~D*( ~C + C ) + A*~B*C*~D + ~A*~C*D* ( ~B+ B )
+ ~A*C*D*( B + ~B )
3. X = A*B*~D + A*~B*C*~D + ~A*D*( C + ~C )
4. X = A*B*~D + A*~B*C*~D + ~A*D
5. X = A*~D*(B + ~B*C) + ~A*D
6. X = A*~D*(C + B) + ~A*D //Second law of Dist.
 |  | 1 | 
 | 1 | 1 | 
1 |  |  | 1
1 |  |  | 1
BA 00 01 11 10
DC
00
01
11
10
Kmap
Kmap
AC~D
~AD
AB~D

## Slide 20: Summary
Gate is a fundamental building block of all digital systems.
Logic gates are expressed with Boolean equation.
K-maps are used to derive Boolean equations from a truth table.
Design a digital system (combinational circuit)
  Draw a truth table.
  Draw K-maps to derive Boolean equations.
  Draw a circuit diagram based on the equations.