## Slide 1: CSS 422 Hardware and Computer Organization
Sequential Circuit
State Machines and Registers
Professor: Munehiro Fukuda
Ver. 2

## Slide 2: Topics
Designing Finite State Machines
  Example 1: Two-bit binary counter
  Example 2: Three-bit sequential circuit
Looking at Typical Sequential Circuits
  Ripple counter
  Shift register
  Storage register
Null Ch3.7

## Slide 3: Design of Finite State Machines
5 Steps
  Draw a state transition diagram.
  Draw a state transition table.
  Simplify redundant states.
  Allocate flip-flops to the states.
  Draw Kmaps to design combinational logics that generates state transitions and outputs.
Timer and Sequencer Design

## Slide 4: Example 1: 2-Bit Binary Counter
An input is a binary number.
Count the number of 1s from 0 to 3, (i.e., 00 to 11) and thereafter reset to 0, (i.e., 00)
Design this sequential circuit.
Sequential Circuit
A
X
1 0 1 1 0 0 1 0
0 1 1 1 0 0 0 0
CLK
Step 1: State Diagram
S0
S1
S2
S3
X=1/A=0, B=1
B
0 1 1 0 1 1 1 0
X=0/A=0, B=0
X=1/A=1, B=0
X=1/A=1, B=1
X=1/A=0, B=0
X=0/A=1, B=0
X=0/A=1, B=1
X=0/A=0, B=1
Timer and Sequencer Design

## Slide 5: Step 2: State Transition Table
 | Input X = 0 |  |  | Input X = 1 |  | 
Current State | Next State | Output A | Output B | Next State | Output A | Output B
S0 | S0 | 0 | 0 | S1 | 0 | 1
S1 | S1 | 0 | 1 | S2 | 1 | 0
S2 | S2 | 1 | 0 | S3 | 1 | 1
S3 | S3 | 1 | 1 | S0 | 0 | 0
Step 3: Simplification Skipped
No States to Merge
Timer and Sequencer Design

## Slide 6: Step 4: State Allocation
 | Input X = 0 |  | Input X = 1 |  | Input X=0 |  | Input X=1 |  | Input X=0 |  | Input X=1 | 
Current State | Next State | Output | Next State | Output | Inputs to JK FF-A |  |  |  | Inputs to JK FF-B |  |  | 
AB | AB | AB | AB | AB | JA | KA | JA | KA | JB | KB | JB | KB
00 | 00 | 00 | 01 | 01 | 0 | * | 0 | * | 0 | * | 1 | *
01 | 01 | 01 | 10 | 10 | 0 | * | 1 | * | * | 0 | * | 1
10 | 10 | 10 | 11 | 11 | * | 0 | * | 0 | 0 | * | 1 | *
11 | 11 | 11 | 00 | 00 | * | 0 | * | 1 | * | 0 | * | 1
Qt | Qt+1 | J | K
0 | 0 | 0 | *
0 | 1 | 1 | *
1 | 0 | * | 1
1 | 1 | * | 0
State | AB
S0 | 00
S1 | 01
S2 | 10
S3 | 11
State allocation to JK FF A and B
JK FF State Transition Table
State Transition Table with JK FF A and B
Timer and Sequencer Design

## Slide 7: Step 5: Karnaugh Maps
0 | 0 | * | *
0 | 1 | * | *
AB 00 01 11 10
X
0
1
Kmap
JA = BX | JB = X
KA = BX | KB = X
* | * | 0 | 0
* | * | 1 | 0
AB 00 01 11 10
X
0
1
Kmap
0 | * | * | 0
1 | * | * | 1
AB 00 01 11 10
X
0
1
Kmap
* | 0 | 0 | *
* | 1 | 1 | *
AB 00 01 11 10
X
0
1
Kmap
Timer and Sequencer Design

## Slide 8: Logic of 2-bit Binary Counter
Timer and Sequencer Design

## Slide 9: Example 2: 3-bit Sequential Circuit
An input is a sequence of 3-bit binary numbers.
If it is a 010, 011, 110, or 111 sequence, the circuit should emit 1 as its output.
Desgin this sequential circuit.
Sequential Circuit
Z
X
111 000 010
1 0 1
CLK
Step 1: State Diagram
S0
S1
S2
S3
S4
S5
S6
X=1/Z=0
X=0/Z=0
X=1/Z=0
X=0/Z=0
X=1/Z=0
X=0/Z=0
X=1/Z=1
X=0/Z=1
X=1/Z=0
X=1/Z=0
X=0/Z=0
X=0/Z=0
X=0/Z=1
X=1/Z=1

## Slide 10: Step 2: State Transition Diagram
 | Input X = 0 |  | Input X = 1 | 
Current State | Next State | Output Z | Next State | Output Z
S0 () | S2 | 0 | S1 | 0
S1 (1) | S4 | 0 | S3 | 0
S2 (0) | S6 | 0 | S5 | 0
S3 (11) | S0 | 1 | S0 | 1
S4 (10) | S0 | 0 | S0 | 0
S5 (01) | S0 | 1 | S0 | 1
S6 (00) | S0 | 0 | S0 | 0

## Slide 11: Step 3: Simplification
 | Input X = 0 |  | Input X = 1 | 
Current State | Next State | Output Z | Next State | Output Z
S0 | S2 | 0 | S1 | 0
S1 | S4 | 0 | S3 | 0
S2 | S6 | 0 | S5 | 0
S3 | S0 | 1 | S0 | 1
S5 | S0 | 1 | S0 | 1
S4 | S0 | 0 | S0 | 0
S6 | S0 | 0 | S0 | 0
Coldwell’s merging rule:
States that transit to the same state and produces the same output can be merged
S35 | S0 | 1 | S0 | 0
S35
S35
S46 | S0 | 0 | S0 | 0
S46
S46

## Slide 12: Step 4: State Allocation
 | Input X = 0 |  | Input X = 1 |  | Input X=0 |  | Input X=1 |  | Input X0 |  | Input X=1 | 
Current State | Next State | Output | Next State | Output | Inputs to JK FF-A |  |  |  | Inputs to JK FF-B |  |  | 
AB | AB | Z | AB | Z | JA | KA | JA | KA | JB | KB | JB | KB
00 | 01 | 0 | 01 | 0 | 0 | * | 0 | * | 1 | * | 1 | *
01 | 10 | 0 | 11 | 0 | 1 | * | 1 | * | * | 1 | * | 0
11 | 00 | 1 | 00 | 1 | * | 1 | * | 1 | * | 1 | * | 1
10 | 00 | 0 | 00 | 0 | * | 1 | * | 1 | 0 | * | 0 | *
Qt | Qt+1 | J | K
0 | 0 | 0 | *
0 | 1 | 1 | *
1 | 0 | * | 1
1 | 1 | * | 0
State | AB
S0 | 00
S1 | 01
S2 | 11
S3 | 10
State allocation to JK FF A and B
JK FF State Transition Table
State Transition Table with JK FF A and B

## Slide 13: Step 5: Karnaugh Maps
0 | 1 | * | *
0 | 1 | * | *
AB 00 01 11 10
X
0
1
Kmap
JA = B | JB = ~A
KA = 1 | KB = ~X + A
* | * | 1 | 1
* | * | 1 | 1
AB 00 01 11 10
X
0
1
Kmap
1 | * | * | 0
1 | * | * | 0
AB 00 01 11 10
X
0
1
Kmap
* | 1 | 1 | *
* | 0 | 1 | *
AB 00 01 11 10
X
0
1
Kmap
Z = AB~X + ABX = AB(~X + X) = AB

## Slide 14: Example 2’s Sequential Circuit

## Slide 15: How about Allocating D FF?
Qt | Qt+1 | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
State | AB
S0 | 00
S1 | 01
S2 | 11
S3 | 10
State allocation to D FF A and B
D FF State Transition Table
State Transition Table with D FF A and B
 | Input X = 0 |  | Input X = 1 |  | Input X = 0 | Input X = 1 | Input X = 0 | Input X = 1
Current State | Next State | Output | Next State | Output | Inputs to D FF-A |  | Inputs to D FF-B | 
AB | AB | Z | AB | Z | DA | DA | DB | DB
00 | 01 | 0 | 01 | 0 | 0 | 0 | 1 | 1
01 | 10 | 0 | 11 | 0 | 1 | 1 | 0 | 1
11 | 00 | 1 | 00 | 1 | 0 | 0 | 0 | 0
10 | 00 | 0 | 00 | 0 | 0 | 0 | 0 | 0

## Slide 16: Kmap and D FF-based Circuit
0 | 1 | 0 | 0
0 | 1 | 0 | 0
AB 00 01 11 10
X
0
1
Kmap
1 | 0 | 0 | 0
1 | 1 | 0 | 0
AB 00 01 11 10
X
0
1
Kmap
DA = ~AB | DB = ~A~B + ~AX = ~A(~B + X)
Z = AB(~X + X) = AB

## Slide 17: D Flip-Flops as a Ripple Counter
A 4-bit binary ripple counter
  Given the name because the pulses “ripple” through the circuit
Clock in
S
R
D
CLK
Q
Q
S
R
D
CLK
Q
Q
S
R
D
CLK
Q
Q
Q1
Q2
Q3
1
RESET
S
R
D
CLK
Q
Q
Q0
Each “D” FF divides the incoming clock frequency by 2X
RESET sets all Q output to 0 without a clock signal (asynchronous)
Counts as fast as the first stage can toggle, but cannot be read until the count has rippled through to the last stage
Can build counter/dividers of any length, any binary divisor
  Clock frequency at output Q3 equals fClock in ÷ 16
Timer and Sequencer Design

## Slide 18: D Flip-Flops as a Shift Register
S
R
D
CLK
Q
Q
Q0
S
R
D
CLK
Q
Q
Q1
S
R
D
CLK
Q
Q
Q2
S
R
D
CLK
Q
Q
Q3
Shift data in
1
Shift data out
Clock in
RESET
Shift register moves data through successive stages on each clock pulse
Used for serial data communications, multiplication ( why ?), image processing
Basis for UART ( Universal Asynchronous Receiver/Transmitter )
Data can be read in serially and then read out in parallel
Serial data communications limits the number of signal wires needed to transmit bytewide
data ( Example shown here is a nibble )
Parallel In Serial Out Device

## Slide 19: D Flip-Flops as A Storage Register
BUS: A grouping of “like” signals Here we have Data In bus ( D0..D7) and Data out bus ( Q0..Q7)
Busses are usually drawn with heavier lines to differentiate them from individual signal wires
CPU Register / Memory Design

## Slide 20: Summary
Understand how to design and implement a finite state machine with flip-flops.
Review typical sequential circuits that are used in computer design.