## Slide 1: CSS 422 Hardware and Computer Organization
Computer Arithmetic
Professor: Munehiro Fukuda
Ver. 3

## Slide 2: Topics
Nagative binary numbers and their arithmetic (Null Ch2.4)
  Signed magnitude
  One’s complement
  Two’s complement
  Multiplication/Division by shifts
Real numbers (Null ZCh2.5)
  Binary
  Fixed point
  Floating point

## Slide 3: Signed Magnitude
Sign
  If positive, then MSB is 0
  If negative, then MSB is 1
Examples
  in 8-bit system: 7 = 0 0 0 0 0 1 1 1 -7 = 1 0 0 0 0 1 1 1
  in 4-bit system: 7 = 0 1 1 1 -7 = 1 1 1 1
Integer Arithmetic
75 + 46 = 121
107 + 46 = 25 (overflow)
How about -43 – (-24)
= -43 + 24 = -19?
1 0 1 0 1 0 1 1
+ 0 0 0 1 1 0 0 0
------------------------
1 1 0 0 0 0 1 1 = -67

## Slide 4: Signed Magnitude
Question (in 4-bit system (nibble))
How to represent zero? 0000 or 1000 ?
Both of them are zero. So we have two zeros.
How many unsigned numbers you can have in a nibble system?
unsigned: 0000 to 1111 (sixteen numbers from 0 to 15),
How many signed numbers you can have in a nibble system?
signed: 0001 to 0111 (positive: 1 to 7), 1111 to 1001 (-7 to -1) , so fifteen numbers including zero. What are we missing?
With this representation in 4-bits sytem,
  What is 7 – 5 in binary?
  01112– 01012= 00102
  What is 7+ (-5) in binary?
  01112+ 11012= 1 01002
  Need to distinguish A + B, -A + B, A + (-B), and -A + (-B)

## Slide 5: One’s Complement
Sign
  If positive, then MSB is 0
  If negative, then MSB is 1
But a given positive number and its negative are in a dual representation
  +3 = 0000 0011
  –3 = 1111 1100
Integer arithmetic
48 + (-19) = 29
carried around
Arithmetic is simpler with 1 carried around
But:
two zeros: positive zero 00000000
negative zero 11111111

## Slide 6: Two’s Complement
Sign
  If positive, then MSB is 0
  If negative, then MSB is 1
But, given a postitive number, its negative number is 1’s complement + 1.
  +3 = 0000 0011
  –3 = 1111 1100 + 1 = 1111 1101
Example: In 8-bit system, compute the 2’s complement of 0x5E in ARM (or $5E in 68K)
  Step 1: Convert to binary: 0x5E = 2_0101 1110 in ARM (or %0101 1110 or 0b01011110 in68K)
  Step 2: Complement bits 1010 0001
  Step 3: add 1 = 1010 0001 + 1 = 1010 0010
  Step 4: Convert to hex again: 2_1010 0010  0xA2
Example: In 2-hexa bit system, compute the 16’s complement of 0x5E in ARM (or $5E in 68K)
  Step 1: Complement bits 0xA1 (= $A1)
  Step 2: add 1 = 0xA1 + 1 = 0xA2 (= $A2)

## Slide 7: Two’s Complement
Question (in 4-bit system (nibble))
How to represent zero? 0000 or 1000 ?
The first one is zero, the second one is -8
How many unsigned numbers you can have in a nibble system?
unsigned: 0000 to 1111 (0 to 15),
How many signed numbers (in 2’s complement) you can have in a nibble system?
Positive: 0000 to 0111 ( 0 to 7)
Negative: 1000 to 1 111 (-8 to -1): So, total 16 numbers
With this representation in 4-bits system,
  What is 7 – 5 in binary?
  01112– 01012= 00102
  What is 7+ (-5) in binary?
  01112+ 10112= 1 00102
  (Since it is 4-bit system, the carry bit won’t appear, so 00102=210)

## Slide 8: Two’s complement arithmetic
Arithmetic overflow:
  Adding two positive number results in a negative number
  Adding two negative number results in a positive number
  How this can be possible?
If the result is out of range, then the computer results in an incorrect answer
For example, in 4-bit system (range is -8 to 7)
  7+ 7 = 0 1 1 1 + 0 1 1 1 = 1 1 1 0 (It is not 14, it is -2) incorrect result, negative
  (-7)+(-8) = 1 0 0 1 + 1 0 0 0 = 1 0 0 0 1 (it has a carry bit and the result is 1) incorrect, positive
How the process detect the overflow? It has special bits to check. (Will cover later)

## Slide 9: Multiplication/Division w/ Shifts
Multiplication by shifting left
1 left shift = x 2
  00001011 (1110) -> 00010110 (2210)
2 left shifts = x 4
  00001100 (1210) -> 00110000 (4810)
3 left shifts = x 8
  00001100 (1210) -> 01100000 (9610)
Division by shifting right
1 right shift = / 2
  00001100 (1210) -> 00000110 (610)
2 right shifts = / 4 ->
  00001100 (1210) -> 00000011 (310)
Then, how about:
5 / 2 = ?
-7 / 2 = ?

## Slide 10: Real Numbers in Binary
Subtraction Method
Multiplication Method
Means larger than 0.5
Means larger than 0.05
Means less than 0.05
Means equal to 0.05
0.812510 = 0.11012

## Slide 11: Real Numbers and Recurring Fractions
Many fractions are repeating
Ex) convert 0.6 to binary, using the multiplication method
  0.6 * 2 = 0.2 ---- 1
  0.2 * 2 = 0.4 -----0
  0.4 * 2 = 0.8 -----0
  0.8 * 2 = 0.6 -----1
  0.6 * 2 = 0.2 ---- 1
  0.2 * 2 = 0.4 -----0
  0.4 * 2 = 0.8 -----0
  0.8 * 2 = 0.6 -----1
  So, 0.6  0.1001100110011001….. (will be repeated infinitely)
  Solution:
  Truncation : The simplest technique. Drop unwanted bits
  Ex) 0.1101101  0.1101
  Rounding : Better technique, but complicated
  Ex) 0.1101101 = 0. 1101 + ( 0.0000101 = 2-5+2-7> 2-6)
  = 0.1101 + 0.0001 = 0.1110

## Slide 12: Real Number in Computers
How to represent a real number in a computer system?
  Real number = integer part + fraction part
  Can we represent an irrational number in binary?
  No, since we have a fixed number of bits, and irrational numbers are irregularly infinite number.
  If we approximate, then we can represent in bits.
  Limited precision
  Overflow/underflow is unavoidable

## Slide 13: Real Number Formats
Two main approaches: Fixed vs. Floating
Fixed-point representation
  Divide the bits for integer part and fraction part
  Point is fixed
  Easier but less flexible
Floating-point representation
  Divide the bits for sign, exponent and mantissa part
  Match with scientific notation
  Point is floating
  Flexible but more complex
  Floating-point is now a standard

## Slide 14: Fixed-Point Representation
Fixed-point representation
  Divide the bits for integer part and fraction part
  For example, 3.62510 = 11.1012
Not flexible.
  What if you really need to represent 3.625 * 10(-18) in computer?
  How many bits will be needed?
    1018 = Exa = Giga * 103 * 103 * 103= 230 * 210 * 210 * 210= 260
    60 bits
0 | 0 | 1 | 1 | 1 | 0 | 1 | 0
Integer part
Fractional part

## Slide 15: Floating-Point Representation
Floating point representation
  Divide the bits for sign, exponent and mantissa
IEEE floating-point format
  IEEE short real or single precision : 32-bits
  IEEE long real or double precision: 64 bits
Sign (1) | Exponent (8) | Mantissa(23)
Sign (1) | Exponent (11) | Mantissa(52)

## Slide 16: Floating-Point Representation
We will mostly use 32-bit (single precision) format.
Let’s represent a real number to floating-point format
  Ex) - 3.812510
  = - 11.11012 (note that the integer part is not 2’s complement)
=-1.11101*21 (normalize: scientific notation)
Sign bit = 1, since negative
Exponent = 1 + 127 (biased) = 128 = 100000002
Mantissa: 11101
Therefore in floating-point representation,
1 100 0000 0 111 01 00 0000 0000 0000 00002 = 0xC0740000 in ARM(or $C0740000 in 68K)
Sign (1) | Exponent (8) | Mantissa(23)

## Slide 17: Normalization and Bias Exponent
Normalization: Always 1 appears as an integer part
  So, we do not have to represent this 1 in the format, therefore save one bit
Biased exponent:
  The exponent has 8 bits, meaning it can range from -127 to 127 (Here we assume that -128 will never happen)
  Therefore if we add 127 to the exponent, it will be always non-negative number.
  So, let’s assume that in the representation, 0~255 is available for exponent filed

## Slide 18: Summary
Why don't computers use signed magnitude?
Why do we want to use two's complement rather than one's complement?
How will shift-based divisions truncate data?
How to convert a real number into binary.
What are the pros and cons of fixed point numbers?
Explain the normalization, the exponent, and the mantisa of IEEE floating-point numbers.