## Slide 1: CSS 422 Hardware and Computer Organization
Introduction to Computer Architecture
Professor: Munehiro Fukuda
This and subsequent slide deck includes a subset of Profs. Arnie Berger and Wooyoung Kim’s materials.
Ver. 3

## Slide 2: Topics
Preface: Course syllabus
  Course objectives
  Course work and grading
  Policies
Lecture 1-1: Introduction to computer architecture
  Von Neuman Architecture and the others
  Levels of computing systems
Lecture 1-2: Data representation in computers
  Number bases and inter-base conversions
  Numbers in computers

## Slide 3: Syllabus
From: https://www.lucidchart.com/blog/use-lucidchart-to-create-visual-syllabi

## Slide 4: Course Objectives
This is an introductory course into..
  Assembly Language Programming
    Programming model of a microprocessor ( ARM Cortex-M )
    Addressing modes
    Writing in assembly language
    Assembling, linking, loading, debugging
    Interfacing (device-drivers, busses)
  Computer memory system and transition to operating system
    Memory hierarchy
    Caches
    I/O processes
    Interrupts, Exceptions
  The architecture of modern microprocessors
    RISC vs CISC
    Pipeline and performance (if time allows)
  The fundamentals of digital hardware (digital logic and circuit design)
    Concepts of gates, flip-flops, registers
    Algorithmic State Machines
    Data path and control flow (heart of a processor)
    Introduction to microprocessors
Lower layer
Upper layer
Textbook Null
Course work 1
Course work 2
Course work 3
Course work 4

## Slide 5: Course Work, Grading, and Policy
Achievements | Estimated Grade
95 – 100 | 4.0
90 – 94 | 3.5 - 3.9
80 - 89 | 2.5 - 3.4
70 - 79 | 1.5 - 2.4
62 - 69 | 0.7 - 1.4
Course Work |  | %
Exams |  | 50
Project |  | 16.5
Participation | In-Class Lab, Exercises 0.5% x 19 sessions | 9.5
Homework (3% x 8 assignments) |  | 24
Total |  | 100
Exams: open book
Project: to be done individually (but not in a group)
Submissions: Canvas only. No email submission
Make-up or late submission policy: sickness, family emergency (but not obligation), business/conference trips, and religious events
Regrading discussions: within 1 week after graded

## Slide 6: Intro to Computer Architecture
von Neuman
  Instructions/data all non-distinguishably stored in memory
Harvard
  Instructions and data separately accessed: e.g. I cache and D cache

## Slide 7: von Neumann Architecture
IR
PC
MDR
Regs
Memory
MAR
ALU
address
data
Instruction
Data
Essence: Everything (incl. instructions and data) in Memory

## Slide 8: Harvard Architecture

## Slide 9: Data Representations
From: http://www.pages.drexel.edu/~nci27/binary-study-guide.html
Why Binary?
Binary, octal, and hexadecimal
Bits, bytes, nibbles, words, and doubles
Giga, mega, kilo, milli, micro, nano

## Slide 10: Represent Data Value as Voltage
Approach #1 | Approach #2 | Apporach #3
along a single electrical conductor | along multiple electrical conductor | Along multiple, parallel, on-off electrical conductor
24.56345
RADIO
SHACK
Zero volts
(ground)
24.56345 V
4.2
RADIO
SHACK
Zero volts
(ground)
2
4
5
6
3
4
5
20
21
22
23
24
25
26
27
28
29
210
211
212
213
214
215
on 1
off 0
on 1
off 0
off 0
on 1
on 1
on 1
off 0
off 0
off 0
on 1
on 1
on 1
on 1
off 0

## Slide 11: Binary Number System
Since we are switching between two voltage levels, our number system has only 2 digits, 1 or 0: a binary number system
The arithmetic and logical operations on a set of binary number is called Boolean Algebra
From approach #3, what is the number:
  off on on on on off off off on on on off off on off on ?
  0 1 1 1 1 0 0 0 1 1 1 0 0 1 0 1 ?
  Answer: 30949
How did I get this?
  0 x 215 = 0 1 x 214 = 16,384 1 x 213 = 8,192
  1 x 212 = 4,096 1 x 211 = 2,048 0 x 210 = 0
  0 x 29 = 0 0 x 28 = 0 1 x 27 = 128
  1 x 26 = 64 1 x 25 = 32 0 x 24 = 0
  0 x 23 = 0 1 x 22 = 4 0 x 21 = 0
  1 x 20 = 1
  16,384 + 8,192 + 4,096 + 2,048 + 128 + 64 +32 + 4 + 1 = 30949

## Slide 12: Binary, Octal, and Hexadecimal
We use the binary number system to represent numbers and logical operations in a computer
Reading and writing binary numbers is tedious and error-prone because the numbers can be very long
Octal and hexadecimal are ways to simplify the representation of numbers to make them easier to understand and manipulate
For example:
  0 1 1 1 1 0 0 0 1 1 1 0 0 1 0 1 = 30,949 in decimal
  0 1 1 1 1 0 0 0 1 1 1 0 0 1 0 1 = 074345 in octal (074345 in C)
  0 1 1 1 1 0 0 0 1 1 1 0 0 1 0 1 = 78E5 in hexadecimal (0x78E5 in C)
Notice how hexadecimal is the most compact way to represent the number
Notice how the binary numbers are grouped together in octal (by 3) and hexadecimal (by 4)
Question: when do you use octal or hexadecimal? Any examples?

## Slide 13: Decimal to Other Bases
Algorithm:
  Example: Convert 73,503 to base 16
  73,503
  16 4,593 ……… 15 (F)
  16 287 ……… 1
  16 17 ……… 15 (F)
  16 1 ……….. 1
  Therefore, answer is 11F1F16
  Why this algorithm?
  11F1F = 1 * 16^4 + 1 * 16 ^3 + F * 16^2 + 1 * 16 + F
  = ((((1 * 16) + 1) * 16 + F) * 16 + 1) * 16 + F
  = ((17 * 16 + 15) * 16 + 1) * 16 + 15 = (287 * 16 + 1) * 16 + 15
  = 4593 * 16 + 15 = 73503

## Slide 14: Bits, Bytes, Nibbles, Words, …
Bit (1)
Nibble (4)
D3 D0
Byte (8)
D7 D0
D15 D0
Half Word (16)
Word (32)
D31 D0
D63 D0
Double, Long Long Int (64)
D127 D0
VLIW (128)
Very Long Instruction Word

## Slide 15: Engineering Notation
In order to represent very large or very small numbers we usually resort to scientific notation:
    For example: Avogadro’s Number = 6.023 x 10 23
      Mantissa = 6.023, exponent = 23
It is common in engineering to use a shorthand version of scientific notation
Replacement values:
Symbol | Power | Symbol | Power
E: exa | 1018 | a: atto | 10–18
P: peta | 1015 | f: femto | 10–15
T: tera | 1012 | p: pico | 10–12
G: giga | 109 | n: nano | 10–9
M: mega | 106 | μ: micro | 10–6
K: kilo | 103 | m: milli | 10–3
Space
Hz
Time

## Slide 16: Computers and Numbers
GB | MB | KB | B
230 = 1024MB = 1GB | 220 = 1024KB = 1MB | 210 = 1024B = 1KB | 20 = 1B
231 = 2GB | 221 = 2MB | 211 = 2KB | 21 = 2B
232 = 4GB | 222 = 4MB | 212 = 4KB | 22 = 4B
233 = 8GB | 223 = 8MB | 213 = 8KB | 23 = 8B
234 = 16GB | 224 = 16MB | 214 = 16KB | 24 = 16B
235 = 32GB | 225 = 32MB | 215 = 32KB | 25 = 32B
236 = 64GB | 226 = 64MB | 216 = 64KB | 26 = 64B
237 = 128GB | 227 = 128MB | 217 = 128KB | 27 = 128B
238 = 256GB | 228 = 256MB | 218 = 256KB | 28 = 256B
239 = 512GB | 229 = 512MB | 219 = 512KB | 29 = 512B

## Slide 17: Summary
What components does a computer system have?
How does the computer represent numbers?
Convert decimal to any base numbers.
Convert any base numbers to decimal.
Binary, Octal, Hexadecimal number conversions.
What is the number of bits for byte, word and long word?
Express 0.00000002456 with scientific notation.