## Slide 1: CSS 422 Hardware and Computer Organization
Bus and I/O
Professor: Munehiro Fukuda
Ver. 2

## Slide 2: Topics
Bus Organization
  Bus arbitration and tri states
Memory-Mapped versus Port-Mapped I/O
  Intel and ARM examples
Interrupt Handling
  Assembly programs to handle interrupts
Direct Memory Access
  Pros and cons of direct memory access

## Slide 3: Bus Organization
How do we manage the
flow of information?

## Slide 4: Bus Collision
Busses were invented in order to simplify the organization and flow of data within computer systems
  Busses allow many devices to connect to the same data path
    Allow for efficient exchange of data between devices
Question: How do I connect outputs together and not get a short circuit?
1
AND
Gate 1
1
1 (5V)
1
AND
Gate 2
0
0 (0V)
BUS
Short circuit ( bus contention)
Actual result will be an indeterminate logic level

## Slide 5: Bus Arbitration
Input(s) a,b,c
Logical
Function
1
Bus control
Close the switch > output connected
Open the switch > output disconnected
Bus
Interface
BUS
Input(s) d,e,f
Logical
Function
2
Connected to bus
Isolated from bus

## Slide 6: Bus Interface Structure: Tristate
Logic
Gate
1 or 0
1 or 0 or HiZ
Bus Interface Gate
Truth table for Bus Interface Gate
INPUT
OUTPUT
Output
Enable
Hi Z: removing the gate
from the circuit
Output Enable INPUT OUTPUT
1
0
1
0
0
0
1
1
1
0
Hi Z
Hi Z

## Slide 7: Memory-Mapped I/O
I/O ports are mapped on the memory address space.
Processor
  Easy implementation
Address decoding
  More complicated
  nWAIT used for slow I/O devices
OS viewpoint
  Can’t cause a trap when a user program accesses I/O ports.
  Yet reserve I/O ports for OS accesses, using M[4:0]
CPU
D0-D31
A0-A31

## Slide 8: Port-Mapped I/O
I/O ports have a seprate space from the memory address space.
Processor
  Distinguishes MOVE and IN/OUT.
  Needs a pin such as IO/~M
Address decoding
  Easy
OS viewpoint
  Can cause a trap when a user program executes IN and OUT.
#00000000
Memory
Space
#FFFFFFFF
#00000000
I/O
Port
#FFFFFFFF
#00008000
Actual Devices
#00009FFF
CPU
D0-D31
D0-D15
I/O Bridge
A0-A31
Mem
IO

## Slide 9: Switching b/w Memory and I/O Address Spaces
IO/~M distinguishes memory and I/O address spaces.
~RD and ~WR are shared among system memory and I/O advices
From Microprocessors and Microcontroler 1-15 8085 Microprocessor Architecture

## Slide 10: Intel Port-Mapped I/O
System bus and I/O buses are separated by GMCH (Graphics and Memory Controller Hub) and I/O Controller Hub.
  Fast system memory versus slow I/O devices
  64-bit memory address space versus 32-bit I/O port space
From Intel 815 Chipset Family Datasheet

## Slide 11: 68K vs ARM Interrupt
Polling versus Interrupt-Driven I/O
  Polling: CPU needs to keep checking an I/O port if the corresponding peripheral is ready.
  Interrupt: CPU can work on a different task while a peripheral needs time to respond back.
Clements: p367
ARM interrupt sequence
  IRQ asserted by a device
  CPU pushes R0-R3, R12, LR, PC, xPSR
  M[4:0] sent back from CPU to NVIC
  CPU jumps to NVIC’s predefined interrupt vector table entry.
68K interrupt sequence
  IRQ asserted by a device
  IACK responding back to the device
  The device presenting the vector# on the data bus.
  CPU pushes the PC/CCR on the stack.
  CPU jumps to the corresponding interrupt handling routine.
https://microcontrollerslab.com/

## Slide 12: CPU’s Interrupt Service
Jump to the corresponding vector table entry
GPIOA_Handler\
PROC
EXPORT GPIOA_Handler [WEAK]
STMFD sp!, {lr}
; do something
MRS R1, PSP
STR R0, [R1]
LDMFD sp!, {pc}
ENDP
(1)
(2)
(4)
(3)

## Slide 13: Direct Memory Access (1)
Programmed I/O
Data read into CPU
  LDR R0, =#0x20000000
  LDR R1, [R0]
    Instruction Fetch * 2
    Read (0x20000000)
Data written from CPU
  LDR R0, =#0x20000004
  STR R1, [R0]
    Instruction Fetch * 2
    Write (0x20000004)
6 memory accesses

## Slide 14: Direct Memory Access (2)
DMA takes care of memory to device or device to memory data transfers.
68K chip family has 68450 DMA Controller (DMAC).
  Two transfer modes:
  1: Dual address transfers
    Read: Read data from memory or device to DMAC internal holding register.
    Write: Write data from DMAC internal holding register to memory or device
  2: Single address transfers
    Read: Transfer data from memory to device
    Write: Transfer data from device to memory
Now we got two bus masters:
  CPU
  DMAC
Clements: p371
 That’s why we need bus arbitration.

## Slide 15: Direct Memory Access (3)
What can CPU perform other activities?
Null: p423
User program A
write(fd, buf, 512);
Request I/O transfer
Resume CPU registers from User stack B
RTE in MC68K, MOV PC, LR in ARM
User program B
Do another computation
Interrupt handling
Resume CPU registers from User stack A
RTE in MC68K, MOV PC, LR in ARM
User program A
Do something right after write( )

## Slide 16: Disadvantages of DMA
Overrun errors
  While DMAC uses the memory bus in cycle steals or burst transfers, either CPU or DMAC may miss time-critical data
  Solution: round robin arbitration
Cache coherency problem
  While CPU maintain a copy of data in its cache memory, DMAC may overwrite its original on DRAM.
  Solution: cache flush.
$123
$123
Cache
CPU
DMAC
DRAM
Bus
$ABC
CPU
DMA
DMA
DMA
CPU
Time critical data 10 20 30
CPU can’t miss 20.

## Slide 17: Summary
Bus arbitration
  Review the role of ~AS and ~CE/OE in memory access as well as the role of ~BR and ~BG.
Memory mapped and port mapped I/O
  Review the advantages of port mapped I/O
DMA
  Review the two advantages brought by DMA.
    BTW, we need CPU cache to run CPU in parallel with DMA. Why?
  Review the two disadvantages when DMA behaves as a bus master.