## Slide 1: CSS 422 Hardware and Computer Organization
CPU Architecture and Assembler
Professor: Munehiro Fukuda
Ver. 3

## Slide 2: Topics
CPU Architecture
  Embedded systems, microcontrollers, and microprocessors Programming
  RISC vs CISC and Harvard vs von Neuman
Memory architecture
  Memory map
  Memory endianness
  Memory alignment
First assembly program
  ARM Instruction Sets
  VisUAL

## Slide 3: Embedded Systems, Microcontrollers, and Microprocessors
Embedded System
Microcontroller
(General computer system)
Microprocessor
What CSS422 studies include
Berger: Hardware and software organization: the software perspective
Tahir: ARM uProcessor Systems
register files
ALU
code/data memory
Busses
I/Os

## Slide 4: Microprocessor
Memory
Peripherals
A0..A31
D0..D31
To be more specific,
there are Din/Dout registers here.

## Slide 5: How Microprocessor Works
C:
  int *data = 0x20000000;
  *data = 5 + 7;
Assembler
  MOV r0, #5
  MOV r1, #7
  ADD r2, r0, r1
  LDR r3, =0x20000000;
  STR r2, [r3]
Machine Code
  F04F 0005
  F0F4 0107
  EB00 0201
  F04F 5300
  601A
To get the corresponding machine code, you can use
https://armconverter.com/
or
Keil uVersion (installed on UW1-310 windwos)

## Slide 6: Instruction Pipelining
Fetch
Decode
Execute
Fetch
Decode
Execute
Fetch
Decode
Execute
Instruction 1
Instruction 3
Instruction 2
Step 1
Step 2
Step 3
Clocks per instruction = 3
Clocks per instruction = 1
Clock
Instruction
reading
Data
writing
Collison on memory

## Slide 7: CPU Architecture: RICS vs CISC Memory Architecture: Harvard vs von Neuman
RISC
CISC
Code
Memory
Data
Memory
Code
Memory
Data
Memory
0x00000000
0x1FFFFFFF
0x20000000
0x3FFFFFFF
ICode Bus
System Bus
System Bus
Simplified hardware
Relying on compilers
Complex hardware
Easy compilation
ARM

## Slide 8: Memory Map
Memory-mapped I/O
ARM Cortex-M3
Port-mapped I/O
Intel

## Slide 9: Memory Endianness
Big-endian order
IBM 360 – z/Architecture
PDP-10
MC68000
  24-bit addresses
    16MB: 0x000000-0xFFFFFF
  3 data widths
    Byte: 8 bits
    Word: 16 bits
    Longword: 32 bits
Little-endian order
Intel x86
AMD65/x86-64
ARM
0x 01ABCDEF
32-bit int
AB
01
CD
EF
0xFF00
0xFF01
0xFF02
0xFF03
memory
CD
EF
AB
01
0xFF00
0xFF01
0xFF02
0xFF03
memory
Memory
0x000000 Byte0 Byte1
0x000002 Byte2 Byte3
0x000004 Byte4 Byte5
0x000000 Word0 MSB Word0 LSB
0x000002 Word1 MSB Word1 LSB
MOVE #$3210, 4 0x000004 0x32 0x10
0x000000 Longword0 MSW
0x000002 Longword0 LSW
0x000004 Longword1 MSW
0x000006 Longword1 LSW
MOVE #$76543210, $8 0x000008 0x76 0x54
0x00000A 0x32 0x10

## Slide 10: Memory Alignment
Half word or Word memory operations, should be applied to only even addresses.
For a misaligned transfer, more than one bus cycle may be required:
  Degrades CPU performance
Instruction words should be aligned on word boundaries: otherwise bus error.
D0
D15
D7
D8
D0
D7
D8
D15
D16
D23
D24
D31
byte0
byte1
byte2
byte3
word0
word1
Longword0
16-bit wide data bus
32-bit wide data bus
byte0
byte1
word0
Longword0-1
Longword0-2
D0
D7
D8
D15
D16
D23
D24
D31
byte0
byte1
byte2
byte3
word0
Longword0
32-bit wide data bus
Longword1
D0
D15
D7
D8
16-bit wide data bus
byte0
byte1
word0

## Slide 11: ARM CPUs
ARM
  For general RISC computer systems
ARM CorTex (Core Texas)
  Cortex-M: for microcontrollers
  Cortex-A: for high-performance applications
  Cortex-R: for real-time applications
http://stringinthemaze.blogspot.com/2012/05/

## Slide 12: ARM CPU Registers
Program status registers (PSR)
Application
Interrupt
Execution
Negative
Zero
Carry
Overflow
Saturation IRQ being handled
ICI/IT: Interrupt–continuable instruction / if—then instruction block
Thumb: 1 in Cortex-M
DSP result’s reached MAX/MIN values.
Multi-cycle instructions to be restarted after an interrupt

## Slide 13: ARM Instruction Sets
ARM processors
  ARM state: 32-bit word aligned instructions providing higher performance.
  Thumb state: 16-bit half-word aligned instructions providing higher instruction code density.
Cortex-M processors
  Thumb2 instruction set
    No state switching
    16-bit instructions and 32-bit instructions to be used together
    ADDS R1, R0, #0x5:
    ADDS R1, R0, #0x123:

## Slide 14: Thumb 16/32-bit Instruction Encoding
https://www.sciencedirect.com/topics/computer-science/conditional-execution
Thumb-2 instructions are identified by their most significant 5 bits being 11101, 11110, or 11111.
For each instruction decoding, refer to
https://developer.arm.com/documentation/ddi0403/ee/?lang=en

## Slide 15: Assembly Programming Basics
Label | Opcode | Operand_1, 2, ... n | ; Comments
begin | MOV | R0, #5 | Move constant 5 to R0
 | MOV | R1, #7 | Move constant 7 to R1
 | ADD | R2, R0, R1 | Store R0 + R1 into R2
 | B | begin | Jump to begin
Four fields per line
  Label: an optional field to determine the address of the corresponding CPU instruction
  Opcode: a mandatory CPU instruction
  Operand: mainly 1-3 operands manipulated by the given opcode
  Comment: an optional comment field
Instruction Set
  Data processing: MOV, ADD, SUB
  Memory access: LDR, STR, LDM, STM
  Branch & control: B, BX, BL, BLX

## Slide 16: First Assembly Program
MOV R0, #0 ; R0 will accumulate the sum
MOV R1, #2 ; R1 will have the update even number
MOV R2, #5 ; the counter for the loop
lbegin
CMP R2, #0 ; If R2 != 0 continue with the next instructions
BEQ lend
ADD R0, R0, R1
ADD R1, R1, #2
SUB R2, R2, #1 ; branch unconditionally to lbegin
B lbegin
lend
Note: this program runs only on VisUAL but need additional code to run on a real Cortex-M processor

## Slide 17: VisUAL
Overview:
  VisUAL supports a subset of ARM instructions: https://salmanarif.bitbucket.io/visual/supported_instructions.html
  Four assembly directives are covered: DCD, EQU, FILL, and END
  Memory views:
    Data views are supported.
    Code views (i.e., machine code) cannot be viewed.
  The code needs additional assembly directives and memory arrangement for running on a real Cortex-M
Instructions:
  Visit: https://salmanarif.bitbucket.io/visual/
  Download the simulator from: https://salmanarif.bitbucket.io/visual/downloads.html
  Run: the first assembly program

## Slide 18: Summary
What is the difference between RISC and CISC?
What deteriorates the performance of instruction pipelining?
What is the difference between memory-mapped and port-mapped I/O?
What is the difference between big and little endian orders?
What happens if a CPU instruction or a data item is not aligned memory?
Why does CPUs in general need status registers?
How can you identify given (half) words in code as a 16 or a 32-bit instruction?
What is the difference between CPU instructions and assembly directives?